C Purlin Forming M/C

C Purlin Forming Machine

Model:C

| Configurations | Manual Uncoiler ,Guiding Platform ,Coil Strip Leveler ,Main Body Of Roll Forming Machine, Electro-Motor, Hole-Punch Device ,Cutting Device ,Hydraulic Station ,PLC Control. |
| --- | --- |
| Control System | PLC Panasonic Inverter |
| Main Frame | 350mm H-Beam |
| Main Power | 18.5 kw |
| Pump Power | 15kw |
| Power Supply | 3-Phase,380V,50Hz |
| Forming Speed | 12-14m/min |
| Hydraulic Pressure | 18-20MPa |
| Forming Size | 80-300mm |
| Feeding Thickness | 1.5-3.2mm |
| Roller Station | 12 Stands |
| Roller Diameter | 80mm |
| Backboard Thickness | 18mm |
| Chain Size | 66mm |
| Cutter Standard | Cr12 |
| Roller Standard | Cr12 |
| Cr-Plating Size | 0.05mm |
| Overall Size | 9500×1400×1350mm |
| Total Weight | 6T |

All technical parameters can be changed,according to user s need.