产品名称：TS100-3履带推土机

产品参数：

| 型号 | Model | Unit | TS100-3 |
| --- | --- | --- | --- |
| 整机重量 | Total weight | kg | 11360 |
| 最大牵引力 | Max towing force | kN | 95 |
| 发动机型号 | Engine model |  | LR6A3LU23/0810E |
| 发动机标定功率/转速 | Engine rated power /speed | kw/ r/min | 81/2300 |
| 发动机燃油消耗率 | Fuel consumption of the engine | g/km.h | ≤220 |
| 发动机最大扭距 | Engine max torque | N.m | 414 |
| 前进1-4档 | Forward 1-4 gears | km/h | 2.6～10.4 |
| 后退1-2档 | Reverse 1-2 gears | km/h | 3.7～6.7 |
| 履带宽度 | Track board width | mm | 720 |
| 接地比压 | Land pressure | kPa | 36.5 |
| 推土铲型式 | Bulldozer blade type |  | 直推铲 |
| 外型尺寸(长×宽×高) | Overall dimension(L×W×H) | mm | 4190×3240×3060 |
| 推土铲(宽×高) | Bulldozer shovel（W×H） | mm | 3240×878 |
| 铲刀最大提升高度 | Blade max lifting height | mm | 830 |
| 铲刀入土深度 | Blade max digging depth | mm | 350 |
| 主离合器 | 常结合干式离合器 |
| 变速箱 | 常啮合斜齿传动，啮合套换挡，机械传动手操纵前进4档、后退2档 |
| 转向离合器 | 干式、多片、碟簧压紧、液压助力分离 |
| 转向制动器 | 干式、带式 |
| 最终传动 | 二级直齿轮减速、飞溅润滑 |
| 中央传动 | 螺旋锥齿轮付 |
| 悬架方式 | 半刚性悬架结构 |
| 托带轮（单侧数） | 1个 |
| 支重轮（单侧数：单·双） | 6个：3个·3个 |
| 履带板（单侧数） | 39片 |
| 油泵形式 | 齿轮泵 |
|  | 操纵阀 |
| 牵引装置 | Towing equipment |  | 摆动式 |

产品说明：

1、本机采用与英国里卡多公司合资技术生产的柴油发动机，符合国家Ⅲ阶段排放要求，噪音低、扭距大、节能环保；

2、主离合器：采用干式、多片结构、常结合主离合器，具有扭距储备大，工作可靠等特点；

3、变速箱：变速箱为4F﹢2R机械换档变速箱，操作简单，维修方便，使用可靠；

4、转向离合器为干式，多片转向离合器，液压助力操纵，易保养，操纵轻便；

5、传动：采用两级、直齿、大模数齿轮传动，具有承载能力强，可靠性高等优点；

6、采用豪华驾驶室，顶置式空调系统(选配），操作空间舒适；

7、可选装直倾铲、角铲、环卫铲等多种工作装置，适用于水电工程，农田改造，河滩和池塘等湿地、泥泞和松软工况环境作业。

1、Engine: Choose the pressure rising engine produced with British Ricardo joint-venture technology, lower oil consumption, stronger torsion, which conforms to National Ⅲ emission standard.

2、Main clutch: Choose dry, multi-disk and constant combining clutch which features big torque reserve and high reliability.

3、Gearbox: Choose 4F+2R mechanical gear-shifting gearbox, simply operating, conveniently maintaining, reliably using.

4、Steering clutch: Choose dry and multi-disk turning clutch, manually operating with hydraulically-assisted, easily maintaining, lightly and conveniently operating.

5、Transmission: Choose two stages, straight teeth, big modulus gear transmission, stronger carrying capacity, and higher reliability.

6、Cab: Adopt the luxury cab, overhead air-conditioning system, comfortable operating space.

7、Environmental conditions: This machine is suitable for high depression wetlands, muddy and soft operating conditions, such as hydropower projects, farmland transformation, riverside and ponds.

8、Optional work device of TS100-3: Straight-tilt shovel, angle shovel， environmentally friendly shovel and so on.